SITE PLAN REVIEW REGULATIONS

SECTION I.		AUTHORITY

Pursuant to the authority vested in the Planning Board by the voters of the Town of Langdon on March 10, 1998, and in accordance with the provisions of 674:43 and 44, New Hampshire Revised Statutes Annotated, as amended, the Langdon Planning Board hereby adopts the following regulations governing the development or change or expansion of use of tracts for nonresidential uses or multi-family dwelling units (more than two units), whether or not such development includes a subdivisions or re-subdivision of the site.

SECTION II.		PURPOSE

The purpose of the Site Plan Review process is to protect the public health, safety and welfare; to promote balanced growth; to promote the timing of development to prevent premature and uncoordinated development of land without the adequate provision of public services and facilities; to ensure sound site utilization; to avoid development which may result in negative environmental impacts; and to guide the character of development.  The Site Plan Review Procedure in no way relieves the developer or his/her agent from compliance with the Zoning Ordinance, Subdivision Regulations or any other ordinance which pertains to the proposed development.  No site plan will be approved until it complies in all respects with any and all pertinent ordinances and regulations.

SECTION III.		SCOPE OF REVIEW

Whenever any development or change or expansion of use of a site governed by these regulations is proposed or whenever any changes are proposed which differ from an existing site plan, as previously approved by the Planning Board; before any construction, land clearing, building development or change is begun; before any permit for the erection of any building or authorization for development on such site shall be granted; the owner of the property or his authorized agent shall apply for and secure from the Planning Board approval of such proposed site development in accordance with procedures outlined in this regulation.

The Planning Board shall have the responsibility for making the final decision as to the necessity of Site Plan Review.  Where there is any doubt as to whether or not a project requires Site Plan Review, the affected party should request a determination from the Board.  In any effort to clarify what constitutes a change of use of sufficient magnitude or impact to trigger Planning Board action, the following guidelines will be observed:

*	If the proposal involves a change of use category, e.g., from residential

to commercial, or from single family to multi-family.

*	If the proposal involves external modifications or construction, including

parking lots.

*	If a change of use or expansion would involve significant impacts

in terms of traffic & circulation, parking, or lighting; for example:

a change from an attorney's office to an accountant's office would

probably not involve significant impact, but a change from a Bed &

Breakfast to a restaurant would.

SECTION IV.	DEFINITIONS

The definitions contained in the Langdon Zoning Ordinance and in the Subdivision Regulations shall apply to the Site Plan Review Regulations.

SECTION V.		APPLICATION PROCEDURE

The application procedures as outlined in the Langdon Subdivision Regulations shall apply to Site Plan Review.

SECTION VI.	SUBMISSION REQUIREMENTS

Every application shall be accompanied by a plat showing information relevant to the proposal.  All plats shall, at a minimum, show the submission items listed below, unless a waiver from any of these is granted by the Board.  All existing conditions shall be drawn in solid lines; proposed conditions shall be drawn in dotted lines.  Two (2) copies of the plat shall be submitted with the application.

A.	Plat Submission Items

1.	Name of project or identifying title; names and addresses of owners of record; and

tax map and lot number.

2.	North arrow, date of the plat, scale appropriate to the scope of the development;

name and address of person preparing the plat; signature block for Planning Board

approval.

3.	Vicinity sketch at an appropriate scale showing the location of the site in relation 			to the existing public streets; and the zoning district(s).

4.	All abutting land owners, physical features and uses of abutting land within 200 			feet of the site.

5.	Boundary lines, their source, approximate dimensions and bearings, and the lot 			area in acres and square feet.  A certified survey may be required, if deemed 			necessary by the Board.

6.	The shape, size, height, location and use of existing and proposed structures 			located on the site and those existing within 200 feet of the site.

7.	Location, name and width of any existing and proposed roads on the property and 			those existing within 200 feet of the site.  New roads shall be constructed in 			accordance with the provisions contained in the Langdon Subdivision 				Regulations.

8.	Location of existing and proposed sidewalks and driveways, with indication of 			direction of travel for any which are one-way.  Both vehicular and pedestrian 			circulation shall be shown.

9.	Identification of access to the site, sight distance at the access point(s), curb cuts 			and proposed changes (if any) to existing streets; and copy of any driveway 			permit(s).

10.	Location and total number of parking spaces; loading spaces and other similar 			facilities associated with the use.

11.	A landscape plan, describing the number, location, types, and size of all

existing and proposed landscaping and screening.

12.	The location, type, and nature of all existing and proposed exterior lighting.

13.	Natural features such as streams, marshes, lakes, or ponds.  Wetlands, as 				defined by USDA county soil surveys.

14.	The existing and proposed grades and topographic contours based on USGS data, 			with spot elevations and base flood elevations where appropriate.

15.	The size and location of all existing and proposed water mains, sewers, culverts, 			to include location and distance to any fire hydrants and/or fire ponds.

16.	Copy of certification by a licensed septic designer that an existing system is

adequate to meet the needs of the proposed use.

17.	Location and type of proposed waste disposal system, with an outline of the 4000 			square foot areas reserved for leach fields for any new system; location of test pits 		and record of percolation tests.

18.	Location of existing and proposed on-site well (showing 75-foot radius).

19.	Soil survey data from the Sullivan County Soil Survey.

20.	Location of any existing or proposed easements, deed restrictions, covenants.

B.	Other

1.	The application shall be accompanied by any necessary Federal, State or local 			permits and approvals, including but not limited to Board of Adjustment, 				Department of Transportation, or Water Supply and Pollution Control 				Commission.

2.	Erosion Control Plan which meets the design standards and specification set forth 			in the "Erosion and Sedimentation Control Design Handbook for Developing 			Areas in New Hampshire’s" (USDA Soil Conservation Service) shall be 				submitted where one or more of the following conditions are proposed:

a.	a cumulative disturbed area exceeding 20,000 square feet;

b.	construction of a road or street;

c.	construction of three or more dwelling units.

3.	An adequate storm water drainage system developed by a certified engineer.

4.	Copies of any proposed or existing easements, covenants, deed restriction, etc.

5.	An impact analysis may be required, which takes into account the following items

to the extent the Board deems applicable:

a.	Demographic Description.

b.	Community Facilities Impacts (sewage disposal, water system, traffic,

schools, public safety, recreation).

c.	Environmental Impact Analysis.

6.	Such other information as deemed necessary by the Board in order to apply the

regulations contained herein.

Should the Board determine that some or all of the above-described information is 		to be required, the applicant will be notified in writing within ten (10) days of the 			meeting at which the determination was made.

C.	"As Built" Plans

Supplemental information may be required by the Board to update the final plat or reflect 	"as built" conditions and details.  The plan shall show any easements and dedicated 	roadways.  A security bond may be required to guarantee performance of the applicant's 	obligations as described herein.

SECTION VII.	DEVELOPMENTS HAVING REGIONAL IMPACT

All applications shall be reviewed for potential regional impacts.  Upon such a finding, the Board shall furnish the regional planning commission(s) and the affected municipalities with copies of the minutes of the meeting at which the determination was made.  The copies shall be sent by certified mail within 72 hours of the meeting.  At least 14 days prior to the scheduled public hearing, the Board shall notify by certified mail the regional planning commission(s) and the affected municipalities of the date, time and place of the hearing, and of their right to appear with the status of abutters to offer testimony concerning the proposal.

SECTION VIII.	SPECIAL FLOOD HAZARD AREAS

A.	The Planning Board shall review the proposed development to assure that all necessary 	permits have been received from those governmental agencies from which approval is 	required by Federal or State low, including Section 404 of the Federal Water Pollution 	Control Act Amendments of 1972. 33 U>S>C> 1334.

B.	The Board shall require that all subdivision proposals and other proposed new 		developments greater than 50 lots or 5 acres, whichever is the lesser, include within such 	proposals base flood elevation data.  Sufficient evidence (construction drawings, grading 	and land treatment plans) shall be submitted so as to allow determination that:

1.	all such proposals are consistent with the need to minimize flood damage;

2.	all public utilities and facilities, such as sewer, gas, electrical, and water systems 			are  located and constructed to minimize or eliminate flood damage; and

3.	adequate drainage is provided so as to reduce exposure to flood hazards.

SECTION IX.	PERFORMANCE GUARANTEE

As a condition of approval, the Planning Board shall require the posting of a performance guarantee in an amount sufficient to defray the costs of construction of streets and public utilities.  The amount of the security shall also include fees to cover the cost of periodic inspections.  At the discretion of the Planning Board, the proposed security shall be reviewd by a licensed engineer.  All costs of such review shall be paid by the applicant.  The security shall be approved as to form and sureties by the Board and the municipal counsel.

Where electric lines or other utilities are to be installed by a corporation, municipal department, or public utility, a letter of intent shall be required stating that the work will be done in reasonable time and without expense to the Town.  Each approved plat shall contain a time limit for the completion of streets and public improvements.  The performance guarantee shall be released in phases as portions of the secured improvements or installations are completed and approved by the Board or its designee, in accordance with the plan approved by the Board.

SECTION X.		GENERAL STANDARDS

A.	Design of development should fit the existing natural and manmade environments with 	the least stress:

1.	Site preparation is to be conducted with minimal disturbance to existing 				vegetation.

Stripped topsoil is to be piled and reused on the site where needed.  A minimum 			of 4 inches of topsoil is to be placed on the disturbed area.  The site shall be 			adequately landscaped, as delineated in a landscape plan.

2.	Landscape treatment shall consist of natural, undisturbed vegetation or features, or 		newly-installed ground cover, shrubs, or trees where appropriate.

3.	Grading and filling must be conducted to minimize the alteration of surface and

subsurface drainage to, toward or across abutting properties, unless the written

consent of the abutting landowner is obtained.

B.	Illumination:

1.	Outdoor lighting shall not glare on abutting properties or on public highways or 			streets.

2.	Indirect lighting should be used on signs advertising goods or services offered on 			the premises.  Blinking or flashing lights or signs are subject to the Town Sign 			Ordinance.

3.	Outdoor lighting is restricted to that which is necessary for advertising and 			security of the property.

C.	Pedestrian Safety	Sidewalks shall be provided for pedestrian traffic to provide 	connection between the main entrances of business, housing or industrial establishments 	and parking areas.  In the event that pedestrian shoppers or employees are reasonably 	anticipated, provision shall be made for sidewalks running from the street line to the 	establishments.  All such sidewalks shall be at least six (6) inches above grade and 		protected by curbing.

D.	Off-Street Parking and Loading Requirements:

1.	Sufficient off-street loading and/or unloading space must be provided, including 			of-street areas for maneuvering of anticipated trucks or other vehicles.  Maneuvers 		for parking and/or loading or unloading must not take place from a public street.

2.	Access, parking and loading areas are to be constructed so as to minimize dust, 			erosion, and runoff conditions that would have a detrimental effect on abutting or 			neighboring properties.

a.	Permeable pavement may be used which might reduce the need for 				installation of drainage facilities to accommodate runoff; however, the 				Board may require that access, parking and loading areas be conventionally 			paved, if deemed appropriate.

E.	Screening:	Appropriate screening/buffers are to be maintained or installed to provide 	privacy and noise reduction to residential areas abutting nonresidential sites;

1.	Buffer strips (10 feet minimum - distance largely dependent upon the density of 			development in the area) must be maintained between proposed use and 				residential uses.  Buffer strip between nonresidential and residential uses must 			contain vegetation which will screen nonresidential uses from sight of the 				residential uses during winter months.

2.	Storage areas must be fenced or screened from on-site or adjoining parking and 			neighboring properties.

3.	Litter (garbage) collection areas must be screened.

4.	The use of either fencing or hedges is permitted.

F.	Street Access/Traffic Pattern:	Access to public streets will meet the requirements of the 	NH department of Transportation and/or the Town of Langdon.  Any new road 		construction shall conform to	the road standards as specified in the Langdon Subdivision 	Regulations.  The internal traffic pattern will accommodate the proposed use, as well as 	providing easy, unimpeded access for emergency vehicles.

G.	Water Supply and Sewage Disposal Systems must be sized to adequately meet the needs 	of the proposed use under the regulations of the NH Water Supply and Pollution Control   	Commission and/or the Town of Langdon regulations. It shall be the responsibility of the 	applicant to provide adequate information to prove that the area of the lot is adequate to 	permit the installation and operation of an individual sewerage disposal system, and that 	existing systems are adequate to serve the needs of the proposed development.

H.	Underground fuel storage tanks shall comply with the standards of the NH Water Supply 	and Pollution Control Division, as set forth in Part Env-WS 411.  NH Code of 		Administrative Rules.

I.	Storm water Drainage;  No increase in the peak flow of surface runoff should be 	permitted if such increased runoff passes beyond the property lines of the parcel upon 	which the development occurs, unless it is within an approved public storm drainage 	system.

J.	Pollution Control:   To avoid undesirable and preventable elements of pollution such as 	noise, smoke, soot, particulate, or any other discharges into the environment which might 	prove harmful or a nuisance to persons, structures, groundwater, or adjacent properties is 	that the applicant will employ the best standards and technology economically available 	at the time.

K.	Where required by law, all buildings shall have access for handicapped persons.

L.	Where appropriate, installation of any new utilities and/or transmission lines shall be 	buried 	underground.

SECTION XI.	REVOCATION OF PLANNING BOARD APPROVAL

An approved and recorded subdivision plat may be revoked by the Board in whole or in part, under the following circumstances: (1) at the request of or by agrement with the applicant; (2) when any requirement or condition of approval has been violated; (3) when the applicant has failed to perform any condition of approval within the time specified or within four years; (4) when four years have elapsed without any vesting of rights and the plan no longer conforms to applicable regulations; or (5) when the applicant has failed to provide for the continuation of adequate security.

SECTION XII.	ADMINISTRATION AND ENFORCEMENT

A.	These regulations shall be administered by the Planning Board.  The enforcement of these 	regulations is vested with the Selectmen.  The Selectmen shall not issue any building 	permit for construction which requires site plan approval until or unless such planned has 	received site plan approval by the Board.

B.	Waivers:  Any portion of these regulations may be waived or modified when, in the 	opinion of the Board, strict conformity would pose an unnecessary hardship to the 	applicant and such waiver would not be contrary to the spirit and intent of these 	regulations.

C.	Penalties and Fines:  Any violation of these regulations shall be subject to a civil fine as 	provided in RSA 676:16 and 676:17, as amended.

D.	Appeals:  Any person aggrieved by a decision of the Planning Board may appeal said 	decision to the superior court pursuant to RSA 677:15, except when a disapproval by the 	Board is based upon non-compliance with the zoning ordinance.

SECTION XIII.	VALIDITY

If any provision of these regulations shall be held invalid for any reason by a court, such holding shall not invalidate in any manner any other provision contained herein.

SECTION XIV.	AMENDMENTS

These regulations may be amended by a majority vote of the Planning Board after at least one (1) public hearing following the notification procedure outlined in Section IV, H&I.

SECTION XV.	EFFECTIVE DATE

These regulations, and any amendments thereto shall take effect upon their adoption, and all other site plan review regulations, or part thereof inconsistent wherewith, are hereby repealed.